## Slide 1: Communications Protocol Microcontroller David Emerson ECE 696
10 Aug 2014
Revision 1

## Slide 2
PC/µC Communications Protocol
The purpose of this presentation is to develop a communications protocol that can be used between a computer and a microcontroller or a microcontroller and another microcontroller.
When developing an embedded system that will communicate with other devices, one of the first things you must do is choose how that system will communicate with the outside world. This will drive the peripherals used on the microcontroller.
For example if the requirement is to use Ethernet to talk to the microcontroller there are several options on the microcontroller side. This first is that the microcontroller has built in hardware to handle the Ethernet communications.
If the microcontroller does not have the hardware, there are other options:
  ENC28J60 - Stand-Alone Ethernet Controller with SPI Interface - Microchip (http://www.microchip.com/wwwproducts/Devices.aspx?dDocName=en022889). This is a standalone IC that handles all of the Ethernet protocols and interfaces with a microcontroller using a Serial Peripheral Interface (SPI).
  SBL2e - Serial to Ethernet Server – Netburner (http://www.netburner.com/products/serial-to-ethernet/sbl2e). This is an Ethernet module that handles all of the Ethernet protocols and interfaces with a microcontroller using standard asynchronous serial communications.

## Slide 3
PC/µC Communications Protocol
If there is a requirement is to use USB to talk to the microcontroller there are several options on the microcontroller side. This first is that the microcontroller has built in hardware to handle the USB communications.
If the microcontroller does not have the hardware, there are other options:
  MCP2210 - USB-to-SPI Protocol Converter with GPIO (Master Mode) - Microchip (http://www.microchip.com/wwwproducts/Devices.aspx?product=MCP2210). This is a standalone IC that handles all of the USB protocols and uses the Human Interface Drivers (HID) drivers that are used by keyboards and mice. The IC interfaces with a microcontroller using a Serial Peripheral Interface (SPI).
  FT232R - USB UART IC – FTDI (http://www.ftdichip.com/Products/ICs/FT232R.htm). This is an USB to serial converter IC that handles all of the USB protocols and interfaces with a microcontroller using standard asynchronous serial communications.
Regardless of the interface type used a method of passing information back and forth between the microcontroller and the computer must be developed.
In order to be as universal as possible this communications protocol must be able to transcend the actual method of passing data, i.e serial, I2C, SPI, parallel, USB, or Ethernet.

## Slide 4
PC/µC Communications Protocol – PC to µC
The following slides show an example of a protocol used to pass information. This protocol is broken down into two separate directions of communication; PC to microcontroller and microcontroller to PC.
Below is a visualization of the structure for the PC to microcontroller communications for this protocol:
The individual parameters are defined below:
  $: “Wake Up” Character: This character is used to indicate to the microcontroller that data is coming in. This can be used to wake a microcontroller out of sleep or when the data line is noisy, such as in the case when the data link is an RF data link, the microcontroller can check the character to determine if the incoming data is valid.
  Command: The Command Code is used to indicate a desired action to be performed by the microcontroller. The command code can be as small as a single byte allowing up to 256 possible commands. There is no upper limit on the number of bytes that the command code can occupy, but it is recommended to be kept as small as possible to meet the desired functionality.
Command
(1 – N Bytes)
Byte Count
(X Bytes)
Checksum*
(2 Bytes)
$
(1 Byte)
Data
(0 – 256X-3 Bytes)

## Slide 5
PC/µC Communications Protocol – PC to µC (Cont’d)
  Byte Count: Number of bytes being sent to the microcontroller (includes data & checksum, if used). The number of bytes used to represent the byte count places an upper limit on the amount of data that can be sent. For example if 1 byte is used for byte count the maximum number of bytes that can be sent is 255; if 2 bytes are used for the byte count then 65535 bytes can be sent. The minimum number of bytes used is 1.
  Data: Data to be sent by the computer to the microcontroller.
  Checksum: The checksum an optional component and is intended to provide a measure of error detection. The checksum is computed using the command code, byte count and all bytes of data being sent. A simple algorithm to compute the checksum is a 16-bit Fletcher checksum. The algorithm for this checksum is shown below and is written in pseudo code.
    FLETCHER16(data, count)
    sum1 = 0
    sum2 = 0
    for i=1 to count
      sum1 = (sum1 + data[i]) mod 255
      sum2 = (sum1+ sum2) mod 255
      return ((sum2<<8) OR sum1

## Slide 6
PC/µC Communications Protocol – µC to PC
Below is a visualization of the structure for the microcontroller to PC communications for this protocol:
The individual parameters are defined below:
  Return Header: The return header is used to indicate what command sequence the microcontroller is responding to. As with the command code the minimum number of bytes used is 1 and there is no upper limit. However the return header size should be kept to the absolute minimum to meet the functionality requirements.
  Byte Count: Number of bytes being sent to the microcontroller (includes data & checksum, if used). The number of bytes used by byte count places an upper limit on the amount of data that can be sent. For example if 1 byte is used for byte count the maximum number of bytes that can be sent is 255; if 2 bytes are used for the byte count then 65535 bytes can be sent. The minimum number of bytes used is 1.
Return Header
(1 – N Bytes)
Byte Count
(X Bytes)
Data
(0 – 256X-3 Bytes)
Checksum*
(2 Bytes)

## Slide 7
PC/µC Communications Protocol – µC to PC (Cont’d)
  Data: Data to be sent by the microcontroller the to computer.
  Checksum: The checksum an optional component and is intended to provide a measure of error detection. The checksum is computer using the command code, byte count and all bytes of data being sent. A simple algorithm to compute the checksum is a 16-bit Fletcher checksum.
For the purposes of providing an example implementation of this protocol the following parameters will be used:
  PC to microcontroller
    Command Code: 1 Byte
    Byte Count: 1 Byte
    Checksum: Not Used
  Microcontroller to PC
    Return Header: 1 Byte
    Byte Count: 1 Byte
    Checksum: 16-bit Fletcher Checksum; 2 Bytes

## Slide 8
Command Code Structure
The command code structure is shown below. Three major functions have been chosen to show examples of sending and receiving information.
The numbers shown in the blue box indicate the command code for the major function, and the numbers below each command indicate a sub-function for the major function. For example in the LED operations, to turn the LED on or off the command code sent would be 0x20 with the data byte used to indicate the required action (1=on, 0=off).
0x2X – LED Operations
0 – Turn LED on/off based on input data Return Header: (0x20)
0x3X – LCD Operations
0x4X – Engineering Operations
0 – Output text to LCD
Return Header: (0x31)
1 – Get Firmware
Return Header: (0x41)
2 – Get Serial #
Return Header: (0x42)
0 – Connected?
Return Header: (0x40)

## Slide 9
Code Structure – LED Operations
The operations within this command group are designed to simply turn the LED on and off and pass the status of the LED back to the controlling computer. A single byte of data in the data field is used to indicate whether to turn the LED on (data[0] = 1) or turn the LED off (data[0] = 0).
The message structure to turn the LED on is below:
And, the return message from the PIC when the LED is turned on is:
The message structure to turn the LED off is below:
And, the return message from the PIC when the LED is turned off is:
Start | Command | Byte Count | Data | Checksum
$ | 0x20 | 1 | 1 | N/A
Return Header | Byte Count | Data | Checksum
0x20 | 3 | 1 | 0x6724
Start | Command | Byte Count | Data | Checksum
$ | 0x20 | 1 | 0 | N/A
Return Header | Byte Count | Data | Checksum
0x20 | 3 | 0 | 0x6623

## Slide 10
Code Structure – LCD Operations
The operation within this command group is intended to send text from the computer interface to the LCD screen connected to the microcontroller. The LCD is a 2-line display, with 16 characters per line.
The message structure to write text to the LCD screen is below:
And, the return message from the PIC when the LCD is written to is:
Start | Command | Byte Count | Data | Checksum
$ | 0x30 | 36 | “32 ASCII text characters plus 4 buffer bytes between lines” | N/A
Return Header | Byte Count | Data | Checksum
0x30 | 3 | 1 | 0x9734

## Slide 11
Code Structure – Engineering Operations
The operations within this command group are designed to allow simple queries to the microcontroller.
The connected command queries the microcontroller to determine if the PC has successfully connected to it. The message structure for this command is below. You will notice that the command does not send any data to the PIC.
The return message from the PIC to the PC is below. The PIC returns a single byte of data , specifically the ‘!’ character and the checksum.
The Firmware command sends a request to the PIC to get the current running firmware on the microcontroller. The structure is seen below:
And, the return packet is shown below. The PIC returns 2 bytes of data (the major and minor revisions) and the checksum.
Start | Command | Byte Count | Data | Checksum
$ | 0x40 | 0 | N/A | N/A
Return Header | Byte Count | Data | Checksum
0x40 | 3 | ‘!’ | 0xE764
Start | Command | Byte Count | Data | Checksum
$ | 0x41 | 0 | N/A | N/A
Return Header | Byte Count | Data | Checksum
0x41 | 4 | Firmware Version: (Major, Minor) | 0x1246

## Slide 12
Code Structure – Engineering Operations
The Serial Number command queries the PIC to determine the serial number of the unit. The structure of the message is shown below:
The return packet from the PIC to the PC is below. The PIC returns a single byte of data, which is the serial number, and the checksum.
Start | Command | Byte Count | Data | Checksum
$ | 0x42 | 0 | N/A | N/A
Return Header | Byte Count | Data | Checksum
0x42 | 3 | Serial Number | 0xCD46

## Slide 13
Communications Protocol - Implementation
The following slides and code show an example of how to implement this protocol scheme in a microcontroller.
The code was developed using Microchip’s XC8 v1.31 C compiler and Microchip’s MPLAB X v2.10 IDE.
The code developed for a PIC18F44K22 and PICProto64 proto-board (PP64B) from microEngineering Labs, Inc. (www.melabs.com). The schematic for the connections is shown on the next slide.
The PIC was programmed using Microchip’s PICkit 3 programmer. This programmer can also be used as an in circuit debugger.

## Slide 14
Communications Protocol Test Hardware
The schematic for the test hardware is show below. A 5V Low Drop Out (LDO) voltage regulator is used to power the PIC and serial LCD.
  An LED is attached to Pin 3 (RA1).
  A serial LCD is attached to a hardware UART on Pin 29 (RD6).
  A USB to serial converter is connected to a hardware UART of Pins 25 & 26 (RC6 & RC7).

## Slide 15
Communications Protocol Test Hardware (cont’d)
The serial LCD is an LCD display from Sparkfun Electronics; Part #: LCD-09395 (https://www.sparkfun.com/products/9395). The LCD is connected to UART 2 of the microcontroller and is configured for a baud rate of 9600 bps, 8 data bits, no parity bit and 1 stop bit.
The computer is connected to the PIC using a USB-to-Serial converter from FTDI; Part #: TTL-232RG-VSW5V-WE (http://www.ftdichip.com/Products/Cables/USBTTLSerial.htm). The converter is connected to UART 1 of the microcontroller and is only using the Rx and Tx pins for communications. The PIC is configured for a baud rate of 19200 bps, 8 data bits, no parity bit and 1 stop bit.

## Slide 16
Communications Protocol - Implementation
The protocol can be implemented using a variety of data types, however for this implementation a structure was used to contain all of the parameters for receiving information from the PC and sending information to the PC.
The structure and variable declarations are shown below:
  typedef struct {
  unsigned char command; // command code
  unsigned char byte_count; // byte count
  unsigned char data[128]; // data
  unsigned short checksum; // checksum
  } protocol;
  volatile protocol rx_data; // initialize data packet for receiving data
  volatile protocol tx_data; // initialize data packet for transmitting data
Not all parts are used within the structure. For example the checksum field in the rx_data variable is not used because a checksum is not sent from the PC to the microcontroller. But the checksum is used when sending data back to the PC.

## Slide 17
Communications Protocol - Implementation
In order to receive the data packet one of two methods could be used, polling and interrupts.
Polling requires that the PIC constantly check the serial port to determine if a byte of data has been received. The drawbacks to this method are that the PIC must stop working on other tasks and check the port. This can lead to slowing down work done on other tasks. Polling can also lend itself to missing data if the port is not serviced fast enough. A fine balance between servicing the port and doing other tasks must be struck.
The second method is using an interrupt service routine (ISR). The ISR is configured to trigger an interrupt when a byte of data is received on the serial port. This has the advantages of not having to break away from running tasks to service the serial port. A drawback to this method is that the ISR can not directly return a variable or accept a variable as an input. Global variables must be used to pass information in and out of the ISR. Also as the number of interrupts increase the complexity of the ISR increases because for this series of PICs there are only two address vectors to handle the ISR’s ( high and low priority interrupts).
The interrupt method was chosen for this implementation of the communications protocol.

## Slide 18
Interrupt Service Routine Code
The ISR routine is shown below:
  void interrupt ISR(void) {
  unsigned char RxData, i;
  if(PIR1bits.RC1IF == 1) // check for cause of interrupt
  {
  PIE1bits.RC1IE = 0; // disable UART1 Rx interrupt
  RxData = RCREG1; // read in data from UART1 register, read clears RC1IF
  if(RxData == '$') // check for start byte
  {
  while(PIR1bits.RC1IF == 0); // wait for another byte of data
  rx_data.command = RCREG1;
  while(PIR1bits.RC1IF == 0);
  rx_data.byte_count = RCREG1;
  for(i=0; i<rx_data.byte_count; i++)
  {
  while(PIR1bits.RC1IF == 0);
  rx_data.data[i] = RCREG1;
  }
  rxd = 1; // set received data flag
  }
  PIR1bits.RC1IF = 0; // make sure UART1 Rx interrupt bit is clear
  }
  } // end of ISR routine

## Slide 19
Interrupt Service Routine Code (Cont’d)
As part of the ISR the first thing to do is to check which interrupt caused the PIC to enter the ISR. Because we are using only one interrupt source this is not necessary but still good practice to do. In this case the interrupt flag is the RC1IF flag in the Peripheral Interrupt Register 1 (PIR1).
The next step is to temporarily disable the interrupt (this keeps the PIC from reentering the ISR prematurely), and then read in the data from the serial port register into a local variable (RxData).
Next the code checks RxData to see if it is equal to ‘$’, which indicates that a data packet is being sent and that the PIC should continue to read in bytes from the serial port.
As each byte is read in it is placed in the corresponding element within the data packet structure. For example the first byte received is placed into the command variable and the second byte received is placed into the byte_count variable of the rx_data structure.
The byte_count value then determines how much more data needs to be read in. After all of the data is read in, the rxd variable is used to indicated that a packet has been received.
The ISR then makes sure that the RC1IF flag is cleared and then exits returning back to the main program.

## Slide 20
Main Code
The main code calls all of the initialization routines to configure the internal oscillator, timers, interrupts, and hardware serial peripherals.
Next the code blinks the LED on and off in 500ms increments and then waits for 1 second. This is done as a visual indication that the PIC is working correctly and the timing can be checked with an oscilloscope to ensure that the timing is working correctly.
After the wait time the PIC then configures the LCD and displays the string “Running!” on the first line of the LCD. This is done to ensure that the LCD is working and that the communications between the LCD and the PIC are working correctly. The code for this sections can be seen below:
  SerOut(LCD_BKLT, 2, 2); // set backlight level
  SerOut(CLR_LCD, 2, 2); // clear LCD
  SerOut(LCD_LN1, 2, 2); // set cursor position to fist line, first position
  SerOut("Running!",8,2); // Display message on LCD
  The SerOut function is a custom function designed to send data using a given serial port. The code for this function will be described later on.

## Slide 21
Main Code (Cont’d)
The code then enters the main loop (while (1)), where the PIC spends the majority of it’s time. The loop begins by checking the rxd variable that will be set in the ISR described earlier. If the rxd variable is not set then the code checks to see if the UART1 receive interrupt is enabled (Peripheral Interrupt Enable 1 (PIE1) register, RC1IE bit = 1). If it is not enabled the code will re-enable it. This bit gets cleared anytime the ISR is entered.
If a packet has been received the code checks the command byte in the rx_data structure using the following code:
  switch(rx_data.command)
  {
  case 0x20:
  .
  .
  .
  default:
  break;
  }
The value of the command variable will dictate which case is entered.

## Slide 22
Main Code (Cont’d)
Once the case statement has been completed the code then clears the rxd variable and re-enables the RC1IE UART1 receive interrupt enable bit with the following code:
rxd = 0; // clear received data flag
PIE1bits.RC1IE = 1; // enable UART2 Rx interrupt
Once complete the main loop then cycles back to the beginning waiting for another data packet to arrive.

## Slide 23
Example Case Statement
The following shows an example of one of the case statements within the main loop. In this example the command code was 0x20:
case 0x20: // turn LED on/off
LED = rx_data.data[0];
tx_data.command = 0x20;
tx_data.byte_count = 1;
tx_data.data[0] = LED;
tx_data = check(tx_data);
send_Packet(tx_data, 1);
break;
This case uses a byte of data to turn the LED on or off. The code then fills in the command, byte_count and the status of the LED in the first element of the data array.
The code then calls the check function to generate the Fletcher checksum and increase the byte count by 2 to account for the checksum. That information is then passed back into the tx_data packet.
Finally the code sends the packet out of the serial port to the computer.

## Slide 24
Auxiliary Functions - putChar
The putChar function is designed to send a single byte of data using the specified hardware serial port. The function is defined below:
void putChar(unsigned char data, unsigned char UART_num)
Input Arguments:
  data: 8-bit data to be sent out using the given serial port
  UART_num: number of the UART to use to send data out
Return Value:
  None

## Slide 25
Auxiliary Functions – putChar (Cont’d)
The putChar function code is shown below:
void putChar(unsigned char data, unsigned char UART_num)
{
switch (UART_num)
{
case 1:
while(TXSTA1bits.TRMT == 0); // Wait for UART buffer to be empty to send data
TXREG1 = data; // transmit data over UART
break;
case 2:
while(TXSTA2bits.TRMT == 0); // Wait for UART buffer to be empty to send data
TXREG2 = data; // transmit data over UART
break;
default:
break;
}
} // end of putChar
The code places the data byte into one of the two available UART transmit registers based on the UART_num variable. Once the TXREG has data in it the hardware automatically begins sending the data based on the UART settings.

## Slide 26
Auxiliary Functions – SerOut
The SerOut function is designed to send multiple bytes of data using a specified hardware serial port. The function is defined below:
void SerOut(unsigned char data[], unsigned char size, unsigned char UART_num)
Input Arguments:
  data: This is a byte sized array of data to be sent out
  size: This is the number of bytes to send out
  UART_num: The number of the UART to use to send data out
Return Value:
  None

## Slide 27
Auxiliary Functions – SerOut (Cont’d)
The code for the SerOut function is shown below:
void SerOut(unsigned char data[], unsigned char size, unsigned char UART_num)
{
unsigned char i;
for (i = 0; i < size; i++)
{
putChar(data[i], UART_num);
}
} // end of SerOut
This function is basically a wrapper for the putChar function

## Slide 28
Auxiliary Functions – check
The check function is designed to calculate the 16-bit Fletcher checksum based on the protocol packet passed in. The function also increases the byte_count variable in the packet by 2 bytes. The function is defined below:
protocol check(protocol chk_data)
Input Arguments:
  chk_data: This input is a structure of type "protocol" which contains the data to perform the checksum calculations on and increase the byte count.
Return Value:
  chk_data: The output is a structure of type "protocol" containing the calculated 16-bit Fletcher checksum and adjusted byte count.

## Slide 29
Auxiliary Functions – check (Cont’d)
The code for the check function is shown below:
protocol check(protocol chk_data)
{
unsigned short sum1=0, sum2=0;
unsigned short i;
chk_data.byte_count = chk_data.byte_count + 2; // increase byte count by 2
sum1 = (sum1 + chk_data.command) % 255;
sum2 = (sum2 + sum1) % 255;
sum1 = (sum1 + chk_data.byte_count) % 255;
sum2 = (sum2 + sum1) % 255;
for(i=0; i<chk_data.byte_count-2; i++) // perform CRC calculations
{
sum1 = (sum1 + chk_data.data[i]) % 255;
sum2 = (sum2 + sum1) % 255;
}
chk_data.checksum = (sum2<<8) | sum1; // 16-bit Fletcher checksum
return chk_data;
} // end of check;

## Slide 30
Auxiliary Functions – check (Cont’d)
The functions follows the Fletcher checksum algorithm outlined earlier in this presentation.
First the code increases the byte count to account for the additional bytes of the checksum value.
Next the code begins the calculations by adding the command byte, then the byte_count byte and then using a loop based on the byte_count to calculate the remaining sums.
Once all of the calculations are complete the code shifts the bits of the sum2 variable and or’s that result with the sum1 variable creating the 16-bit checksum value. This value is then placed into the checksum variable of the chk_data structure.
Finally the code returns the chk_data structure back to the calling code.

## Slide 31
Auxiliary Functions – send_Packet
The send_Packet function is intended to send the entire contents of a protocol packet to the requesting computer using the specified serial port. The function is defined below:
void send_Packet(protocol send_data, unsigned char UART_num)
Input Arguments:
  send_data: This input is a structure of type "protocol" which contains the data
  to send using the specified serial port.
  UART_num: The number of the UART to use to send data out
Return Value:
  None

## Slide 32
Auxiliary Functions – send_Packet (Cont’d)
The code for the send_Packet function is shown below:
void send_Packet(protocol send_data, unsigned char UART_num)
{
unsigned char i;
putChar(send_data.command, UART_num); // send command byte
putChar(send_data.byte_count, UART_num); // send byte count
for (i = 0; i < send_data.byte_count-2; i++)
{
putChar(send_data.data[i], UART_num); // send data bytes
}
putChar(send_data.checksum>>8,UART_num); // send first 8 MSB's
putChar(send_data.checksum&0x00FF,UART_num); // send last 8 bits
} // end of send_Packet
The function uses the putChar function to send each of the elements of the send_data protocol structure.

## Slide 33
Communications Protocol
There are many ways to communication between devices. The example protocol shown here is just one example.
When developing a method of communications the key thing the remember is structure. Define the structure early in the process. This helps with determining how the information will be sent and how to parse the information on the receiving end.
Also, make the protocol robust. The more robust, the more applications it can be used in. This keeps you from having to recreate a new protocol for every new application.

## Slide 34
REFERENCES
PIC18(L)F2X/4XK22 Data Sheet; Document #: DS41412F; Microchip
MPLAB XC8 C Compiler User’s Guide; Document #: DS52053B; Microchip
Checksum. (2014, August 7). In Wikipedia, The Free Encyclopedia. http://en.wikipedia.org/w/index.php?title=Checksum&oldid=620248688
Fletcher's checksum. (2014, July 20). In Wikipedia, The Free Encyclopedia. http://en.wikipedia.org/w/index.php?title=Fletcher%27s_checksum&oldid=617651338